## Slide 1
Course Name: FPGA Laboratories
Course No: ECE 128 Term: Fall 2024
Course Instructor: Jannatun Naher, PhD

## Slide 2: Numbering Systems and Adder Designs

## Slide 3: Number Representation
Recap: data formats in Verilog
– syntax: <size>'<radix><value>;
– Radix: O for octal, b or B for binary, d or D for decimal, h
or H for hexadecimal
– Other than 0 and 1, value can also be x (unknown) and z
(high impedance), but can not be negative
More examples
– 5’O37 // 5-bit octal
– 7’Hz // 7-bit z extended to zzzzzzz

## Slide 4: Binary Codes
Processors typically compute in binary form, but
input and output can be encoded in other form
Binary coded decimal
– Use four binary bits for one decimal digits with the weight
of 8-4-2-1
Gray code
– Minimize bit flips in adjacent values
Hamming code
– Increase hamming distance between any pair of valid codewords to detect errors

## Slide 5: Decimal, BCD, and Gray Code

## Slide 6: Decimal, BCD, and Gray Code

## Slide 7: Seven Segment Displays
Fig. An un-illuminated seven-segment display and nine illumination patterns corresponding to decimal digits.

## Slide 8: Seven Segment Displays
Anode is controlled by PMOS (0=ON)
– An anode is shared among all segments of one display
• Each segment is a light-emitting diode (LED)
– Anode connect to Vhigh and Cathode = 0, light ON
– A cathode is shared among multiple displays

## Slide 9: Segment Converter

## Slide 10: Hierarchical (Modular) Design
Divide a system into smaller parts
– Test smaller part one by one
– Reuse and replicate parts
An example of converting Gray code to BCD, and then to seven segment display

## Slide 11: Skeleton of the Verilog Code

## Slide 12: Adder Design

## Slide 13: Implementation of a Full Adder

## Slide 14: Implementation of a Full Adder

## Slide 15: 2-Bit Adder

## Slide 16: Latency of Addition
Latency of combinational logic is the time between input occurs and output becomes stable
Critical path: the path between and input and output with the maximum delay determine the latency of combinational logic
The RCA has a long critical path
– Carry at each bit position depends on the calculation of the carry at previous bit position
– Example
c_out_1 = b_1&c_in_1|a_1&c_in_1|... = b_1&c_out_0|a_1&c_out_0|...;
– The critical path increases linearly with the width of the adder
Latency of combinational logic can be input and last input dependent

## Slide 17: Alternative: Carry Lookahead Adder

## Slide 18: How to Convert Codes?
Combinational or sequential logic?
– Output depends on input only
– Each output depends on multiple input bits
Step 1: write truth table for each output bit
Step 2 (optional): use Kaurnaugh map to derive simplified combinational logic for each output
Step 3: implement in Verilog

## Slide 19
Sum-of-Products circuit: focus on inputs states where truth table is a 1.
Product-of-Sums: focus on input states where truth table is a 0.
Minterm: a product term that includes each input of a circuit or its complement.
Maxterm: A maxterm is a Boolean expression resulting in a 0 for the output of a single cell expression, and 1s for all other cells in the K-maps
SOP & POS

## Slide 20: Max & Min Terms
Max Terms
Min Terms

## Slide 21: More Examples for K-Maps (4 bit Prime Numbers)
F(d,c,b,a) is true if input d,c,b,a is prime

## Slide 22: Design 4 bit prime numbers (using K maps)

## Slide 23: Design 4 bit prime numbers (using K maps)

## Slide 24: Design 4 bit prime numbers (using K maps)

## Slide 25: Short-cut way: